## Slide 1: Coal treatment and emissions control technologies
Dr. Tanveer Iqbal

## Slide 2: Coal treatment
Environmental impact dependent on the specific technology for Energy generation
Environmental Concerns
  water resource
  pollutant emissions
  waste generation
  public health
  safety concerns or all of these.

## Slide 3: Coal treatment
Mined coals are highly heterogeneous varying widely in quality and content from
  country to country
  mine to mine
  even from seam to seam.
Coal is normally associated with ash-forming minerals and chemical material including
  sand,
  rock,
  sulfur and
  trace elements.
These impurities affect the properties of coal and the combustion process including the stack (flue) gas emissions and byproducts of combustion.

## Slide 4: Coal treatment
Coal cleaning and washing at the mine or at the power plant (or at both) removes ash, rock, and moisture from coal to the extent possible.
In principle, coal is crushed and washed when it is cleaned at the mine preparation plants which removes the largest amount of sulfur found in coal.

## Slide 5: Coal treatment Processes
Pre-combustion
Combustion
Post-combustion
Conversion technologies

## Slide 6: Pre-Combustion Technologies
The cleaning and washing of coal
Coal benefaction, coal beneficiation or coal preparation process
Improves the quality of coal
Provides benefits
  savings in the transportation, and in capital and operating costs of the power plant, particularly the boiler, coal handling and ash handling systems, and
  reduction in the cost of power generation if the washed coal increases the plant load factor and the washery rejects are utilized efficiently in fluidized bed boilers

## Slide 7: Pre-combustion processes (coal benefaction)
Physical cleaning or washing
Chemical cleaning
Biological methods of cleaning – to remove sulfur and ash
also includes drying, briquetting, and blending

## Slide 8: Physical cleaning
Separates effectively ash content, rocks and pyritic sulfur and trace elements like mercury from the coal.
Done using water
The density differences are exploited to separate coal from the impurities.
Each type of coal has its own wash ability criteria depending on the chemical composition.
When coal is crushed and washed, the heavier impurities separate from the coal, making it cleaner.
Since coal can be ground into much smaller sizes similar to powder, it allows for removal, up to 90% of the pyritic sulfur.

## Slide 9
Typical Coal Cleaning Plant
Process Flow diagram

## Slide 10: Conventional Physical Coal-cleaning Technologies
Crushing
Pulverizing coal and sieving into coarse, medium and fine particles.
Jigs (G)
Separating medium size particles from coarse ones.
Dense-medium baths (G)
Separating medium size from coarse particles.
The non-organic material is released during crushing which can be
separated due to their dense nature by further processing.

## Slide 11: Conventional Physical Coal-cleaning Technologies
Froth floatation
Separating fine (<0.5 mm) particles by selective attachment of air bubbles to coal particles allowing them to be buoyed up into a froth while leaving the rest of the particles in water; for fine particles, it relies on surface properties of ash vs coal.
Cyclones (G)
Used for coarse to medium particles
Wet concentration
Rapid shaking causes particles of different densities to migrate to different zones on the table’s periphery

## Slide 12: Conventional Physical Coal-cleaning Technologies
Concentration spiral
Electrokinetics
Physical cleaning is accomplished by using electrophoresis method in which the electrokinetically charged particles in a liquid are migrated toward an electrode of opposite charge in a dc electric field.
As the coal pulp is fed from the top of the spiral, it flows downword, and the centrifugal force causes the separation

## Slide 13: Advanced Cleaning Processes
Advanced physical cleaning
Advanced froth floatation (S), Electrostatic (S), & Heavy liquid cycloning (G)
Aqueous phase pretreatment
Bioprocessing, Hydrothermal, Ion exchange, Selective agglomeration & Spherical oil agglomeration.

## Slide 14: Advanced Cleaning Processes
Organic phase treatment
Depolymerization, Alkylation, Solvent Swelling, Electrolysis & Rapid pyrolysis
Other processes
Microwave, Microbial desulfurization, Fluidized bed, Ultrasonic, Liquid-fluidized bed classification, Chemical cleaning processes, Dry benefaction, & High gradient magnetic separation.

## Slide 15: Chemical cleaning
Chemical cleaning is used to remove organic sulfur from the coal
Molten-caustic leaching
  Coal is immersed in a chemical that actually leaches the sulfur and other minerals from the coal
Biological cleaning involves using microorganisms (bacteria) that literally ‘eat’ the sulfur out of the coal

## Slide 16: Benefits of pre-drying
Power plants that use high-moisture coals suffer from efficiency decrease. The efficiency is estimated to decline by 4% if the moisture-content in the coal increases from 10% to 40% and by 9% if the moisture-content increases to 60%
High moisture increases coal-handling feed rate and requires extra energy for coal-handling systems leading to an increase in the costs for plant operation and maintenance

## Slide 17: Coal pre-drying using low grade Heat
overall plant efficiency is increased due to increase in boiler efficiency, thereby reducing CO2 emissions,
boiler size and plant’s extra power usage are reduced by reducing the flow rates of coal and flue gas,
flow rate reduction also allows extra SO2 capture for high sulfur content coals by extra scrubber,
NO2 emissions are reduced by increasing coal’s heating value and reducing the flow rates of coal and air,
Hg oxidation increases during combustion and this oxidized Hg can be removed by wet-lime spray towers,
using low-grade or waste heat avoids the need for alternative heat sources.

## Slide 18: EMISSIONS CONTROL TECHNOLOGIES - Used during combustion
Remove sulfur dioxide and nitrogen oxides
Fluidized-bed combustion is one such technology.
In fluidized-bed combustion, finely grounded coal mixed with limestone is injected with hot air into the boiler.
This bed of coal and limestone suspends on jets of air and resembles a boiling liquid, a ‘fluid’.
As the coal burns, the limestone acts as a sponge and captures the sulfur.

## Slide 19: Fluidized-bed combustion

## Slide 20: Post-combustion processes
Schematic design of an absorber in a Flue Gas Desulphurization System

## Slide 21
Dry scrubber system using slaked lime slurry

## Slide 22: NOx control methods
Low excess air (LEA) combustion
Low NOx Burners (LNB)
Staged Combustion (SC)
Flue Gas Recirculation (FGR)
NOx Reburning
Selective catalytic reduction (SCR)
Selective Non-catalytic Reduction (SNCR)

## Slide 23: Selective catalytic reduction (SCR)

## Slide 24: Selective Non-catalytic Reduction (SNCR)